## Slide 1: Internet protocol (part 4: Routing)
Rocky K. C. Chang
Chung Yuan Christian University
Dept. Information and computer engineering
March 29, 2023

## Slide 2: The routing problem
Problem: How can a router/host determine the path to a destination (i.e., the route)?
Any routing protocol must allow routers to make a corporate, consistent, and correct local forwarding decisions regarding any destination in a global routing fabric.
  Sources and destinations are generally not directly connected.
  Routers are generally not directly connected.

## Slide 3: Design issues
Scalability: scale to the number of networks
  Routing table size
  Routing messages
  Time to converge
Free of permanent/transient routing loops
Optimal paths: hop count, type-of-service, quality-of-service, etc.
Security
Host mobility and perhaps router mobility

## Slide 4: Design choices
Centralized vs decentralized
  A central processor computes the routes.
Source-based vs hop-by-hop
  E.g., source routing and destination-based routing
With or without the global topological info.
  E.g., OSPF vs RIP
Dynamic (or state-dependent) vs static routing
  IP routing vs ATM routing
Single-path vs multiple path

## Slide 5: Levels of routing
Intra-domain routing (inside AS) vs inter-domain routing (inter-AS)
AS: Autonomous system (AS number or ASN)
Not all routers are equal.
  Interior routers: Only know how to route datagrams to destinations within the same AS.
  Border routers: Interface between its AS and other AS’s:
    A nonbackbone router usually has a “default route” to another “more knowledgeable” router for “unknown destinations.”
    A default-free router is supposed to know every “IP network” in the Internet.

## Slide 6: Autonomous system
Autonomous system (AS): A set of networking resources governed by a single administrative authority.
AS’s can be classified into
  Stub AS: has only a single connection to one other AS, and it only carries local traffic.
  Multihomed AS: has connections to more than one other AS, but refuses to carry transit traffic.
  Transit AS: has connections to more than one other AS, and is designed to carry both transit and local traffic.
AS number: 1659 for TANet and 4616 for PolyU
Nodes: AS; links: peer-peer, provider-consumer

## Slide 7: Exercise 1
Traceroute to 103.16.128.2 and find out how many ASes are involved. Find out their ASNs.
These tools are useful:
  http://whois.tanet.edu.tw/
  https://www.whatismyip.com/ip-whois-lookup/
  https://hackertarget.com/as-ip-lookup/
  https://www.ipvoid.com/ip-to-asn/ (use this for IPASN)

## Slide 8: Exercise 2
Perform traceroute from https://perfops.net/traceroute-from-australia (Brisbane) to your machine.
What are the similarities and differences between this reverse traceroute and the forward traceroute obtained in the last slide?

## Slide 9: Exercise 3
Repeat the last two exercises for www.net.princeton.edu.
The reverse traceroute can be performed from https://www.net.princeton.edu/traceroute.html.

## Slide 10: Exercise 4
TANet is a single AS.
What is its ASN?
What are the IP addresses under this AS?
  https://bgp.he.net
  Wiki TANet

## Slide 11: Exercise 5
Go to https://bgp.he.net/net/140.135.0.0/16#_netinfo
Click at AS 1659 to view various information about this AS.
Find out the route propagation paths from AS 1659 to other ASes.

## Slide 12: Exercise 6
Go to https://stat.ripe.net/ and type in 140.135.0.0/16. What new information do you find about this address block?
Go to https://stat.ripe.net/widget/bgplay and visualize the route to 140.135.0.0/16.
Try the above for Taiwan Central University and observe the differences.