## Slide 1: 1. Preliminaries
Rocky K. C. Chang
February 15, 2023

## Slide 2: Outlines
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 3: What is Internet/computer network?
A network of computers
Computers
  Hosts (autonomous)
  Routers/switches
  Others: middleboxes, firewalls, NAT box, etc
Often modeled as a graph
  Nodes (interface or (a group of) host/routers)
  Links (physical or logical)

## Slide 4: Lumeta (Global Network Visibility)

## Slide 5: http://www.treehugger.com/files/2009/05/what-is-the-environmental-impact-of-the-internet.php

## Slide 6: https://www.pccwglobal.com/en/global-coverage

## Slide 7: http://en.wikipedia.org/wiki/File:Internet_Connectivity_Distribution_%26_Core.svg

## Slide 8: Exercise
Search for a list of Internet exchanges in the world.
What is the “ranking” of the TPIX (Taipei Internet Exchange)?

## Slide 9: https://www.inacon.de/ph/data/IPv4/IP-Protocol-Stack_OS_RFC-791.htm

## Slide 10: Exercise
Find out the full names of FTP, HTTP, SMTP, SNMP, POP3, DNS, and DHCP.

## Slide 11: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 12: Classifications of computer networks
According to the network size:
  Interconnection networks: connecting multiple processors
  Body area networks (BAN)
  System/Storage area networks (SAN): connecting processors to storage servers
  Sensor networks
  Local area networks (LAN): connecting a limited number of hosts in a close proximity
  Metropolitan area networks (MAN): connecting a limited number of LANs in a close proximity
  Wide area networks (WAN): connecting hosts situated anywhere

## Slide 13: Classifications of computer networks
According to mobility:
  Fixed networks
  Wireless networks
  Mobile networks
According to the network speed:
  Dial-up networks (kbps)
  High-speed networks (Mbps)
  Gigabit networks (Gbps)

## Slide 14: Classifications of computer networks
According to the “system software”:
  Novell NetWare (IPX) (obsoleted)
  IBM’s SNA (?)
  Xerox’s XNS (obsoleted)
  DEC’s DECnet (obsoleted)
  Apple’s AppleTalk (obsoleted)
  Microsoft’s NetBIOS and NetBEUI
  TCP/IP

## Slide 15: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 16: What are your expectations for a computer network?

## Slide 17: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 18: What is the Internet?
Why built an Internet?
How to build it?
Who built it?
Who owns and governs it?
Who continues to develop the technologies?
Who manages the domain names and IP addresses?
Source: https://en.wikipedia.org/wiki/History_of_the_Internet#ARPANET

## Slide 19
Source: http://joaobordalo.com/files/topInternetHistory.png

## Slide 20: Content
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 21: A “nuts and bolts” view
millions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)

## Slide 22: A “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, SIP, CSMA/CD
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
Home network
Institutional network
Mobile network
Global ISP
Regional ISP

## Slide 23: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery

## Slide 24: What’s a protocol (πρωτόκολλον)?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 25: What’s a protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 26: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 27: A closer look at network structure:
Network edge: applications and hosts
  access networks, physical media: wired, wireless communication links
Network core:
  interconnected routers
  network of networks

## Slide 28: The network edge:
End systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server
peer-peer
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Skype, BitTorrent

## Slide 29: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 30: Digital Subscriber Line (DSL)
telephone
network
DSL
modem
home
PC
home
phone
Internet
DSLAM
Existing phone line: 0-4KHz phone; 4-50KHz upstream data; 50KHz-1MHz downstream data
splitter
central
office
  Also uses existing telephone infrastructure
  XDSL, X = A, RA, H, V, S, …
  dedicated physical line to telephone central office

## Slide 31: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 32: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 33: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 34: Fiber to the Home
ONT
OLT
central office
optical
splitter
ONT
ONT
optical fiber
optical fibers
Internet
Optical links from central office to the home
Two competing optical technologies:
  Passive Optical network (PON)
  Active Optical Network (PAN)

## Slide 35: Ethernet Internet access
100 Mbps
100 Mbps
100 Mbps
1 Gbps
server
Ethernet
switch
Institutional
router
To Institution’s ISP
Typically used in companies, universities, etc
  10 Mbs, 100Mbps, 1Gbps, 10Gbps Ethernet
  Today, end systems typically connect into Ethernet switch

## Slide 36: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b/g/n/ac (WiFi): 11/54/600/1000Mbps
wider-area wireless access
  provided by telco operator
  ~1Mbps over cellular system (EVDO, HSDPA)
  WiMAX (10’s Mbps) over wide area
  LTE
base
station
mobile
hosts
router

## Slide 37: Exercise
Find out the physical (or MAC) addresses of your notebook’s WiFi adaptor and Ethernet adaptor using ipconfig –all.

## Slide 39: Exercise
Do a traceroute (tracert on WIN) to a local host, such as www.sinica.edu.tw, www.post.gov.tw, google.com.tw, etc.
  Which “hops” belong to the edge and which belongs to the core?
Repeat the above for hosts outside Taiwan, such as my alma mater RPI (www.rpi.edu), or your favorite university.

## Slide 40: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 41: The Network Core
Mesh of interconnected routers
The fundamental question: how is data transferred through the net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 42: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 43: Network Core: Circuit Switching
Network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 44: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 45: Network Core: Packet Switching
Each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
Resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 46: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, bandwidth shared on demand: statistical multiplexing.
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 47: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) packet of L bits on to link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
transmission delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 48: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at the same time is around .0004
Packet switching allows more users to use network!
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 49: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem

## Slide 50: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately

## Slide 51: AT&T POP Level Network in the US (2013)
Source: https://www.researchgate.net/publication/259673301_A_Novel_Approach_to_Interior_Gateway_Routing/figures?lo=1

## Slide 52: Google’s network
Source: https://ppc.land/google-network-will-be-expanded-with-3-new-submarine-cables-and-cloud-with-5-new-regions/

## Slide 53: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.

## Slide 54: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 55: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 56: A real example

## Slide 57: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 58: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 59: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 60: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 61: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 62: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 63: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 64: Exercise
Ping google.com.tw and find out the performance of the network path from your machine to the destination.
Find out the locations of the hops on the path.

## Slide 65: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 66: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 67: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 68: Exercise
Try out a number of speedtest services:
  http://www.myspeedmeter.net
  https://www.speedtest.net
  https://www.speedcheck.org

## Slide 69: Outline
What is a computer network?
How to classify a computer network?
What are your expectations for a computer network?
What is the Internet?
  The Internet structure
      Network edge
      Network core
  Network performance
  Layered model and protocols

## Slide 70: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 71
HTTP
TLS/SSL
TCP
158.132.1.1
172.217.163.227
IP
IP
IP
IP
802.11
Ethernet
https://www.google.com.hk/
https://www.google.com.hk/
TCP port
TCP port
IP address
IP address
MAC address
MAC address

## Slide 72: exercise
Take any packet captured by your Wireshark. How many protocol layers are included in that packet?

## Slide 73: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
DEcapsulation

## Slide 74: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
DEcapsulation

## Slide 75: Generic layering and protocols
Each protocol defines two interfaces:
  Service interface: the operations that local objects can perform on the protocol.
  Peer interface: the form and meaning of messages exchanged between protocol peers to implement the communication service.
Protocol entity
Protocol entity
Message format and interpretation
Services
Services
Protocol entity
Protocol entity
Message format and interpretation
Services
Services

## Slide 76: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 77: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 78: The Internet's hour-glass model
…
FTP
HTTP
NV
TFTP
TCP
UDP
IP
NET
1
NET
2
NET
n
Application
Transport
Network
Data-link
http://www.artofteachingscience.org/?p=291

## Slide 79: Conclusions
We looked at general issues, such as the definition of a computer network, classifications of computer networks, and expectations from them.
For the Internet, we looked at the current Internet structure, network performance, and layered model and protocols.
In the coming lectures, we will examine the internetworking (layer 3), transport layer (layer 4) very briefly and datalink issues (layers 1-2).

## Slide 80: Acknowledgments
Most of the slides are obtained from the slides provided by Computer Networking: A Top Down Approach, 5th edition by Jim Kurose, Keith Ross.

## Slide 81: “I think the press has a tendency to pick a person and paint them 10 feet tall. In fact, each of us does a little piece and I’ve done one thing, people add on that and then another. So you get credit for doing the whole damn thing, and that’s not so.” — Paul Baran, after receiving the National Medal of Technology and Innovation

## Slide 82
"Let love and faithfulness never leave you; bind them around your neck, write them on the tablet of your heart. Then you will win favor and a good name in the sight of God and man." (Proverbs 3:3-4)
"不可讓慈愛誠實離開你，要繫在你的頸項上，刻在你的心版上。 這樣，你在 神和世人眼前，必蒙恩寵，得著美名。" (箴言 3:3-4)

## Slide 83: end