## Slide 1: Ch. 25, 26 UDP, TCP
CS332, Fall 2017
Victor Norman

## Slide 2: UDP
Q: What functionality does UDP provide that IP does not already provide?
A: Identification of the payload being carried at layer 5.
I.e., a port # so that it can hand the data off to an application.
I.e., demultiplexing.

## Slide 3: Message-oriented interface
Q: What does it mean that UDP has a message-oriented interface?
A: It means when a program (at layer 5) tells UDP (at layer 4) to send data, the data is sent in one message to the destination. (We’ll see that TCP uses a different paradigm.)
This also means that when you send the data via a SOCK_DGRAM socket, the packet on the wire will be the size you sent (if it isn’t fragmented).

## Slide 4: Fragmenting UDP?
Q: Multiple people asked about UDP fragmentation. Is it done or not?!
A: UDP does not do fragmentation. You can send a 64KB UDP message. It will be handed to IP below it, and IP will fragment it to fit into the MTU of the network it will be sent out on. The receiving IP layer will reassemble the 64KB packet before handing it back up to the receiving UDP layer.

## Slide 5: Fragmentation vs. Efficiency
Q: If larger messages are efficient but in UDP, large messages cause fragmentation, what usually is the compromise?
A: You want the largest message possible such that they aren’t fragmented. 

## Slide 6: Message vs. streaming services
Q: We learned early on about message vs. streaming services. Is this implemented by UDP and TCP, respectively?
A: Yes, exactly.
Q: Why are there these two choices only: unreliable message-based service, and reliable stream-based service? Why isn’t there a reliable message-based service?
A: Good question. I don’t know why this dichotomy existed initially. There are reliable message-based services now: RTP, e.g. It is actually based on UDP but provides some of the same reliability mechanisms as TCP.

## Slide 7: UDP used?
Q: Is UDP used today?
A: Yes, it is. It is used by
DNS (domain name resolution)
games
streaming live video
etc.
Q: Why is it used?
A: 1) Efficiency. It adds almost no functionality/overhead on top of IP. 2) You can broadcast a UDP message (because UDP is connectionless).

## Slide 8: Pseudo-headers
Q: Why does UDP use part of the IP header in its pseudo-header, when computing the checksum
A: I don’t know.
Q: Is the header transmitted?
A: No. It is built in memory just for error checking.
Q: What about UDP over IPv6?
A: A pseudo-header is still used, with the 32-bit addresses replaced by the IPv6 128-bit addresses.

## Slide 9: UDP broadcasts
Q: Why can you broadcast UDP messages, but not TCP?
A: Think of the complexity of guaranteeing delivery to multiple destinations – and, in fact, an unknown number of destinations.
What happens if one destination stops acknowledging packets?
What happens if one processes packets much more slowly?

## Slide 10: What are the important characteristics of TCP?
Connection-oriented
Point-to-point
Full duplex
Reliable
Uses ports to identify applications using TCP.

## Slide 11: What does TCP assume it gets from the layer below?
Connection-less
Point-to-point
Simplex
Unreliable delivery

## Slide 12: What does connection-oriented mean?
End points must communicate first and set up the virtual connection.
No data is sent until that’s finished.
End points must gracefully tear down the connection.

## Slide 13: What does a Virtual Connection mean?
The endpoints set up and maintain all the state of the “connection” – the middle devices (routers, NATs, etc.) know nothing about it.
As opposed to a circuit through a network in which all devices must participate.

## Slide 14: What does point-to-point mean?
One application talks to one application
  one IP/port to one IP/port
Note: multiple TCP connections can go to the same IP/port. A connection is defined by the 4-ple.

## Slide 15: What does full duplex mean?
Both applications on the endpoints can transmit at the same time.
When a TCP connection is setup, it is full duplex – i.e., each endpoint can stream data.
  If you only want to stream one direction, you have to close the other half – although ACKs, etc., will still be sent.

## Slide 16: What does reliable delivery mean?
Gets the data there
  quickly
  correctly (without errors)
  in order
  completely

## Slide 17: What kinds of problems does TCP have to be able to handle?
Very unreliable delivery from IP.
  Duplicate packets.
  Packets out of order.
  Errors in packets.
Differing speeds of end points.
End point reboot.
Delay from when network changes radically.

## Slide 18: How does TCP handle all this?
Unreliable delivery from IP?:
  checksum the data (eliminate bad data)
  keep track of which bytes have been sent and which have been received, and resend missing bytes
  “positive acknowledgement and retransmission”
  A timer is started for each packet that is sent.
    if the timer expires for an ACK is received for the packet, the packet is resent.

## Slide 19: How does TCP handle all this? (part 2)
Different speeds of end points?:
  (Two problems: how much data an end point can handle at once, and how long it takes to handle it.)
  End points constantly communicate how much more data they can still handle at that time (called “window advertisement”).
  This is “flow control”.

## Slide 20: How does TCP handle all this? (part 3)
End point reboot? (Or application on an endpoint restarts.)
  Every connection is given a unique identifier and packets with that id are only accepted.

## Slide 21: How does TCP handle all this? (part 4)
Delay from network changes radically: consider this:
  end points want to get data through as fast as possible (in general).
  Usually end points want data to flow consistently, not bursty.
  When network “goes down” for a bit, the more data that is “in transit”, the more has to be retransmitted.
  This problem is very complex. Called “congestion control”.

## Slide 22: Congestion Detection
Congestion is detected by…
  increased round-trip time (data  ack) (due to reduced throughput)
  timeouts (due to lost packets, perhaps)
The reaction is to reduce the window size and increase the per-packet timeout value.

## Slide 23: Congestion Collapse
Q: What is congestion collapse?
A: Congestion collapse is when congestion happens in a bottleneck in the network (usually a router), and the router discards packets. When the endpoints detect it, they retransmit, which only makes more traffic at the bottleneck, which causes more dropped packets and more retransmits. …

## Slide 24: Flow control vs. Congestion Control
Flow control via a sliding window allows multiple packets (“segments”) to be sent before any ACK is received. This increases bandwidth utilization (i.e., “speed”).
Congestion control reduces the amount of traffic being sent to avoid congestion collapse.
Both are done by manipulating the window size on a TCP connection.
Also, the ACK timer timeout value can be changed.
  ”Adaptive retransmission”.

## Slide 25: TCP fight between performance and reliability
(Section 26.6, 26.7)
We want our data to flow quickly AND reliably.
Increase window size  data rate increases.
Increase window size  chance of congestion increases.
Congestion  retransmitted packets  more congestion.
  “Congestion collapse.”

## Slide 26: TCP and IP
Q: What is the relationship between TCP and IP?
A: A TCP header and payload is the payload of an IP packet. The IP packet’s type field says it is carrying TCP. In other words, TCP is encapsulated in IP.
TCP builds a virtual connection between the endpoints, using the unreliable IP. IP is responsible for moving the packets to the destination machine.

## Slide 27: Fragmenting IP and TCP
Q: If a packet carrying TCP is fragmented during delivery, and one fragment is lost, how does TCP handle this?
A: 1) IP does fragmentation, when a packet is too large for one hop across the network.
2) If the fragment is lost, IP gives up on the packet and drops it.
3). If the TCP sender does not get an Ack before it times out, it resends the packet (which will get fragmented again).
4) When all fragments are received, the data is sent up to the TCP layer. It will then send an Ack.

## Slide 28: Stream protocol
Q: What does it mean that TCP is a stream protocol?
A: When an application (layer 5) sends a UDP packet, the packet going across the wire contains all the data from the application, in one chunk.
When it sends data using TCP, TCP is free to send as many or few bytes in a packet as it feels it can. The receiver also gets as many bytes at a time as TCP can give it.
The data “flows” from sender to receiver, but the endpoints don’t know how the data is “chunked” when sent across the network.
This is quite inconvenient because most TCP clients are sending fixed-size message back and forth, not streams of data…

## Slide 29: Sample sendall() code.
int sendall(int s, char *buf, int *len)
{
int total = 0; // how many bytes we've sent
int bytesleft = *len; // how many we have left to send
int n;
while (total < *len) {
n = send(s, buf + total, bytesleft, 0);
if (n == -1) {
break;
}
total += n;
bytesleft -= n;
}
*len = total; // return number actually sent here
return n == -1 ? -1 : 0; // return -1 on failure, 0 on success
}

## Slide 30: Receiving…
From Beej’s website:
“What happens on the receiver's end when part of a packet arrives? If the packets are variable length, how does the receiver know when one packet ends and another begins? Yes, real-world scenarios are a royal pain in the donkeys.”
You make sure the first thing in the packet/message is a type or length of the message, so that you code can read a fixed # of bytes, and then figure out how many more bytes it has to read to get all the data in the message.

## Slide 31: Congestion control
Q: Could you explain how TCP controls congestion better? How does reducing the buffer size or window size reduce the data rate? Wouldn't it still send packets of the same size? Can the window size get bigger if there is little traffic or is it initialized to a maximum size?
A: The window size will be decreased  one packet can carry all the data  fewer packets generated  less contribution to congestion. TCP also increases the timeout values.
TCP slowly increases the window size when it doesn’t encounter congestion.

## Slide 32: Flow Control
Q: Is flow control used quite often?
A: Yes: flow control is built into TCP. It, as well as, congestion control, are implemented with the sliding window feature.

## Slide 33: Calvin and Congestion Control
Q: Does Calvin use any of these dynamic congestion control methods?
A: Yes! You use it too – in the TCP/IP software in the OS on your machines.
And Calvin’s firewalls/etc. change some values to slow down youtube bandwidth, etc… 

## Slide 34: Lost window/segment
Q: If data lost in TCP, does the specific segment, or the whole window have to be retransmitted?
A: A window in TCP is a number of bytes, not packets (Comer used packets as an illustration). So, if a segment (a packet) is lost, that segment must be retransmitted.

## Slide 35: Handling reboots/outages
Q: What would happen if a connection was interrupted by an outside glitch on one of the computers (e.g., power outage)?
A: The TCP sender will stop receiving ACKs, will retransmit a few times, and then give up and return an error to the application.

## Slide 36: 3-way Handshake
Q: Can you explain the 3-way handshake more?
A: Yes! The initiator sends a SYN packet (a packet with the SYN flag set), and includes its ID and window size. The responder sends a SYN-ACK response including its ID and window size. The initiator sends an ACK back. (And, I think it piggybacks data in that packet.)

## Slide 37: Old Slides

## Slide 38: Handling slow hosts
Q: How does the sliding window method help the slow host keep up?
A: The slow host will ack more slowly, so the sender will send more slowly. The low-memory host will also send smaller window advertisements.

## Slide 39: Multiple users of one connection?
Q: Is it possible for a connection to transfer data for two or more applications on each computer?
A: Each connection is for one application.

## Slide 40: Choosing an ID
Q: How does the protocol software determine an appropriate ID and a "reasonable time" until that ID can be reused again? (Is it usually/always time-based?)
A: I think it picks a random 32-bit number for each connection. 2^32 is a big number so it is unlikely to repick the number.