## Slide 1: Ch. 28 Q and A
CS 332
Fall 2017

## Slide 2: A little quiz
Q: What is network latency?
Changes in delay and duration of the changes
time required to transfer data across a network
amount of data that can be transferred, per unit time.
A: 2.

## Slide 3: Another little quiz
Q: What do we call the amount of data that can be transferred per unit time? And what units do we use to measure it?
A: capacity, in bits per second.

## Slide 4: Access vs. Queuing Delays
Q: What is the difference between access and queuing delays?
A: Access delays is waiting for others to be quiet so that you can send without collisions. Or, waiting for your transmission slot to come around again (in TDM).
Queuing delay is a packet sitting in a queue of packets, waiting to get to the front of the queue to be sent.

## Slide 5: Average size of the delays
Q: How do the five different kinds of delays compare in terms of average length?
A: I’d have to guess on these…
server delay < propagation delay < switching delay < access delay < queuing delay.
This is a total guess.

## Slide 6: Goodput
Q: Can you provide a better definition of goodput?
A: Maybe…
Goodput is the amount of layer 5 data that gets through per unit time. Throughput is the total # of bits that get through per unit time.
Small packets  lower goodput.
Larger headers  lower goodput.

## Slide 7: Capacity and throughput
Q: What is the relationship between these two?
A: Capacity is the maximum throughput possible. (by definition, but not used consistently in the book or in my speaking…)

## Slide 8: Propagation delay vs. throughput
Q: If propagation delay is a constant, how can networks have varying throughput? I.e., if 10 Mbps and 100 Mbps both use cat5e copper, how can they provide different throughputs?
A: It depends on how efficiently the data can be encoded (and especially decoded) on the medium.

## Slide 9: Specifying throughput
Q: If Calvin has two links to the Internet (through US Signal), each at 500 Mbps, what is the capacity of our link to the world?
A: Hard to say. It could be 500 Mbps or 250 Mbps, or 1000 Mbps depending on the connection type, contract, etc.
This demonstrates the difficulty of specifying throughput.

## Slide 10: Network perf == 6th layer?
Q: In a sense, would it be fair to say that network performance is almost a sixth layer in the stack? That is, since it is supposed to provide info regardless of application (layer 5), is it kind of another layer?
A: I don’t think so. I think of layering as strictly encapsulation – header and payload from one layer becomes the payload of the layer below.

## Slide 11: Heisenberg?
Q: Is it fair to say that there is a kind of Heisenberg Uncertainty Principle in network performance measurement? That is, the fact that you are measuring affects what you are measuring, so it is impossible to get a totally objective measurement?
A: You could almost say that, because, yes, it is hard to get a measure of network performance by using the network.

## Slide 12: Buy more throughput?
Q: How can you buy more throughput?
A: Upgrade your service plan. At home I can get 4 Mbps or 8 Mbps or 12 or 20 or 40…
Done by buying more virtual channels from the ISP. The channels are used in parallel to send bits. Thus, more throughput.

## Slide 13: Asymmetric routes
Q: The book mentions asymmetric routes as a difficulty for network measurements. How does it make it difficult?
A: Traffic from client to server could take one route and traffic from server to client could take another longer or shorter route. So, round-trip time is accurate but does not represent either half correctly.

## Slide 14: Jitter (1)
Q: What units are used to specify jitter?
A: I don’t know… Must be time units.
Q: How do you measure jitter?
A: You look at the arrival time of consecutive packets (assuming the packets are sent out with consistent timing).

## Slide 15: Jitter (2)
Variation in delay. Lower jitter is better.
  “Jitter is the change in latency from packet to packet. RFC 4689 defines jitter as the absolute value of the difference between the forwarding delay of two consecutive received packets belonging to the same stream.”
Easier or harder than delay to measure?
  Do not need to know delay to compute variation of delay.
  Just need to measure packet-to-packet change.
Notes: http://www.lightwaveonline.com/articles/2008/04/measuring-jitter-accurately-54886317.html

## Slide 16: Quiz
Q: If all packets in a stream have the same delay, what is the value of the jitter?
A: 0

## Slide 17: Jitter vs. Delay
Q: Is high amounts of Jitter worse or better then high amounts of Delay?
A: Worse, probably.

## Slide 18: Why keep utilization relatively low?
Q: I found it interesting that most ISPs try to keep their total utilization threshold under 50%. Why do this?
A: It leaves room for bursty traffic – which will happen. Also, consider the formula that estimates current delay: D = D0 / (1 – U).

## Slide 19: Delay and Throughput
Q: Are delay and throughput independent or not?
A: Theoretically independent, but practically not.
Traffic on one link: independent.
Traffic flowing across multiple links: dependent.

## Slide 20: Delay-throughput product
Q: Can you give an example of when you would care about the delay-throughput product?
A: Sure!
Q: What is the definition of it?
A: How much data is “in transit” at a time.
Why is it important? Can mask long delay by putting lots of data in the pipeline.
If link goes down, you lose lots of data, and have to retransmit lots of data.

## Slide 21: Use average?
Q: Since traffic is bursty, do people use an average? What measurement do they use? The delay-throughput product or just admit data traffic is kind of spotty?
A: I think an average is common – or an average and a maximum.

## Slide 22: Old Slides

## Slide 23: Q3
Q3: What is "access delay"? (Hint: you see it when using an Ethernet NIC.)
A: The time for a packet to get access to the network.

## Slide 24: When are delay and throughput not independent?
Over a single network (LAN), delay and throughput are independent.
But, over a series of LANs with switches/routers in between, they become related.
  Queuing delay in a switch leads to lower throughput.
  Queuing delay caused by busy links.
Effective delay D = D0 / (1 – U)

## Slide 25: Q5
Q: What is the capacity of a 10base100 Ethernet line?
A: 100 Mbps

## Slide 26: Q6
Q: If Calvin has two links to the Internet (through US Signal), each at 500 Mbps, what is the capacity of our link to the world?
A: Hard to say. It could be 500 Mbps or 250 Mbps, or 1000 Mbps depending on the connection type, contract, etc.

## Slide 27: Q7
Q: How does throughput compare to goodput?
throughput is the same as goodput
throughput is always less than goodput
throughput is sometimes less than goodput and sometimes more than goodput
throughput is always more than goodput
All of the above.
A: 2.

## Slide 28: Q9
Q: Throughput and delay are theoretically independent. Explain why they are practically dependent on each other.
A: When congestion occurs along a route (at an "intersection"), then packets going along that route will be delayed and throughput will go down.

## Slide 29: Q10
Q: What is the significance of the delay-throughput product?
A: It is a measure of how much data is in transit at any one time. It is significant because if there is a connection problem, then all the data that is in transit at one time that has to be retransmitted.

## Slide 30: 5 Parts of Delay
Q: Can you explain the 5 types of delay a bit more?
A: Sure:
Propagation Delay: delay of moving a signal across a network – even light does not travel infinitely fast.
Access Delay: a device waiting for a cable/fiber to be “clear” before it can send.
Switching Delay: routing a packet.
Queuing Delay: delay from statistical multiplexing
Server Delay: (not really networking) time for a server to formulate a response to a query.

## Slide 31: A No-Delay Network
Q: Would it be theoretically possible to create a network with no delay?
A: Yes! Using quantum physics.
Or not…

## Slide 32: Measuring delay
Q: How can we measure and print out the delay of a packet or packets moving across a network?
A: This is hard! Perhaps…
You measure round-trip times.
  Divide by 2, but then assumes delays are identical each direction – which is not true most of the time.
Put timestamps into the packets.
  But, these are not that useful.

## Slide 33: Throughput vs. Goodput
Q: Can you explain goodput better?
A: Sure!
Goodput is the measure of how much *data* can be sent over the network – not including any network protocol overhead.
E.g., Link has 200 Bps max – throughput. But, its
layer 2 header is 100 bytes. So, only 100 Bps max of *data* can get through. Throughput is 200 Bps; goodput is 100 Bps.

## Slide 34: The Road Analogy
Q: Can you explain the road/traffic analogy more?
A: Why, yes. Yes, I can.
Delay is theoretically independent of capacity.

## Slide 35: Real-time Protocols and Jitter
Q: How do real-time protocols account for jitter?
A: Read chapter 29. 
Example: sending real-time video over the internet – Facetime or Skype.
First, why not use TCP?
RTP sends timestamps in each packet, so users of RTP can implement a jitter buffer.
Packets are released from the buffer with no jitter.

## Slide 36: Isochronous networks
Q: Can you explain isochronous networks?
A: Not really. But, it must be a network that sets up / reserves bandwidth and processing capacity across each hop in the network before traffic flows (circuit-switching).
E.g., Multiprotocol Label Switching (MPLS) or ATM (Asynchronous Transfer Mode) at Layer 2.

## Slide 37: Goodput
Q: Can you clarify "Goodput"?
A: Goodput is how much data gets through per unit time. It is throughput – overhead… (sort of).
Q: How is goodput measured?
A: You could transfer data and see how much gets through in a certain amount of time. Or compute max goodput on paper, if you know exactly the overhead of the protocols.

## Slide 38: Bandwidth, throughput, latency, delay, goodput… Arrrgggh!
Q: What does "bandwidth" really mean?
A: Bandwidth is how much data can get through the network per unit time – how much can be “pushed” through the network.
Q: What about analog bandwidth?
A: I’m not really sure about this…

## Slide 39: Cable vs. Satellite ISP
Q: If a satellite internet company and a cable internet company advertise the same network speed, say 5 mbps, would the effective data rate of the satellite network be slower because of more latency?
A: The bandwidth could be the same, but the delay is probably going to be much longer for the satellite, just because of propagation delay.

## Slide 40: Measuring throughput
Q: Is throughput measured solely on the hardware in the network, for example 1Gbps ethernet?
A: You can measure the throughput of a link, but it is much more interesting to measure the throughput of a network – or a path through multiple networks.

## Slide 41: Jitter
Q: What exactly is jitter?
A: Jitter is the variation in delay for a set of packets. If packets are sent out, say 1 every 1 ms, but arrive with differing gaps, that’s jitter. If one gap is 1ms, the next 2 ms, the next 0.5 ms, etc… that’s jitter.

## Slide 42: Importance of formula 28.1
Q: What is the significance of formula 28.1?
A: It helps estimate delay based on utilization. Utilization is how busy a network is – how many packets are queued up to get sent.

## Slide 43: Measuring network performance
Q: What other methods are there for measuring the network performance apart from ping? Is ping a good indicator for the “speed” of the internet between 2 hosts?
A. ping measures RTT (round-trip time), i.e., delay, which is an important metric. Other tools are: mtr, SNMP, ttcp, iperf, etc.

## Slide 44: Making up for jitter
Q: p 476. The internet uses real-time protocols to compensate for jitter. Could you explain how that is done in a nutshell?
A. The Real-time Transport Protocol (RTP) is sort-of half way between UDP and TCP. There are reliability mechanism in place like TCP, but data is dropped/skipped if it goes missing (retransmission is useless for real-time). Also, the protocol buffers data at the receiver so that it can deliver it consistently when it has enough data.

## Slide 45: Over-booking?
Q: In the book it talked about most network admins not utilizing a network higher than 90%, is this the case with moth ISPs? I feel the service comcast or at&t provides varies wildly from hour to hour. Is this a result of them over booking their network?
A: I have no idea. Could be. But, the internet is very bursty, as Comer says.