## Slide 1: Chapter 22 Q and A
Victor Norman
IS333
Spring 2016

## Slide 2: Quiz
Q1: Explain what connectionless delivery means.
Q2: Explain how the source IP address in a packet is used during packet forwarding.
Q3: Where is the next-hop IP address found in an IP packet?

## Slide 3: IP packet lengths
Q: Is there a minimum length for an IP datagram?
A: Yes. The minimum length is 20 bytes (20 byte IP header, 0 bytes of data). The maximum length is 65,536 bytes (max value that can be represented in a 16-bit field).

## Slide 4: TTL Field
Q: What exactly is the TTL field, and is it similar to the reassembly timer?
A: The TTL field is the number of times the packet can be forwarded before it should be discarded. Aka the number of “hops” it can traverse. Each router decrements its value.
It is unrelated to the reassembly timer.

## Slide 5: Finding matches in the forwarding/routing table
Q: Can you explain the algorithm in section 22.7 better?
A: The equation is (for entry i in the table): if mask[i] & destAddr == dest[i]: forward packet to nexthop[i].
mask[i] & destAddr gives the network portion of the packet’s dest addr – which is what routing is based on.
nexthop[i] is the next router (or the ultimate destination) to see the packet to.

## Slide 6: Why LPM?
Q: Why does forwarding software choose to forward entries with the longest prefixes (and therefore more specific), first?
A: It makes sense. If you had to forward a package to somewhere in South Grand Rapids, and you were told you had two choices – send it to Grand Rapids, or South Grand Rapids, you’d choose the more specific one.

## Slide 7: Longest Prefix Match
Example: suppose you have a router with a LAN on interface eth1: 192.168.3/24. But, you have the CEOs machine, 192.168.3.99, on interface eth7. Your routing table should look like this:
Dest Mask Gateway/NextHop
192.168.3.0 24 direct, eth1
192.168.3.99 32 direct, eth7
default 0 eth2 (rest of network)

## Slide 8: Host-specific routes
Q: How is host-specific routing different from “normal” routing (how does it make it more efficient)?
A: The forwarding algorithm is not different. A host-specific route is chosen because it has the longest prefix (/32).
(Just like the default route is chosen only if nothing else matches, because it has the shortest prefix (/0).)

## Slide 9: Forwarding
Q: Do forwarding algorithms (for Internet forwarding tables) ever change, or do they simply get longer?
A: Forwarding tables do change size, theoretically. On hosts and most routers they probably don’t change very often, if ever. They are based on the IP addresses assigned to interfaces, and a default route, which usually comes via DHCP or a routing protocol (which we haven’t talked about).

## Slide 10: Routing table entries
Q: How are routing table entries added?
3 ways:
  get default route from DHCP when machine boots up.
  When an interface is added (manually or via DHCP), a route is added for all “directly connected” machines.
    When done manually, you specify the IP address and mask for the interface.
  Routers run route-distribution protocols to share routes with each other.

## Slide 11: Typical MTU sizes
Q: How big are MTUs, normally?
A: From a Microsloth website:
Network | MTU (bytes)
16 Mbps Token Ring | 17914
4 Mbps Token Ring | 4464
FDDI | 4352
Ethernet | 1500
IEEE 802.3/802.2 | 1492
PPPoE (WAN Miniport) | 1480
X.25 | 576

## Slide 12: Fragmentation Algorithm
Q: How does a host/router fragment packets?
A: It puts the most data it can in each fragment, leaving the rest for the last fragment (even if it is only 1 byte).

## Slide 13: Reassembly Timer
Q: What is the typical duration of a reassembly timer?
A: On Ubuntu, it is 30 seconds. On Windows, it is 60 seconds.
Q: What is it?
A: It is how long a host holds packet fragments before giving up on receiving them all.

## Slide 14: Reassembly Handling
Q: What happens if a packet cannot be reassembled in time? Does the sender/receiver receive a notification?
A: No. There are no notifications because IP delivery is best-effort.

## Slide 15: Universal and Virtual Packet
Q: I’m somewhat fuzzy on what this “universal” and “virtual” packet is that Comer talks about. Can you explain?
A: Comer just means that each machine must format packets the same way – totally hardware independent – and these packets are then sent over hardware-dependent layer 2s.

## Slide 16: Fields in IP header
Q: What happens to fields in the IP header that are not needed? Are they just skipped, or are they filled with something?
A: They are filled with something – usually 0s. You cannot skip fields or the reader of the packet won’t be able to figure out how to read it.

## Slide 17: Old Slides

## Slide 18: Connectionless?
Q: Could you explain what connectionless service is more clearly? Every host must 'connect' to a network somehow. Is the term 'connectionless' therefore not a bit of a misnomer?
A: Connectionless means that no end-to-end setup or tear-down of the connection is done – i.e., it is not a “circuit”. Packets are just sent and forwarded hop-by-hop to the destination.

## Slide 19: Forwarding/routing?
Q: Is the forwarding table the same as the routing table?
A: Yes. Same thing.
Q: How is each hop determined by the destination IP?
A: Each router looks at the packet’s dest IP address and consults its routing table to figure out where to send the packet next.

## Slide 20: IP datagram vs Hardware frame
Q: What is the difference between an IP datagram and a hardware frame? Is it just that one uses as IP address and one uses a MAC address?
A: Both are “PDUs” – protocol data units. IP calls its stuff a “datagram”. The datagram is sent down to layer 2 to be encapsulated in a layer 2 “frame” to be sent over the local network.

## Slide 21: Best-effort Delivery
Q: In the Best-Effort Delivery, what does it mean that “IP is designed to run over any type of network”? And, how is IP “best-effort”?
A: It means that IP was designed to operate over networks that provide few guarantees. It does not require absolutely perfect, fast, robust layer 2 hardware/protocols. It just requires that the lower layer do its best to deliver the frames correctly. And, it will do the same.

## Slide 22: TTL field
Q: Can you explain the TTL field?
A: Each packet’s TTL (time-to-live) field is initialized to 64 (recommended). Each time a router forwards a packet, it decrements the TTL value. If the TTL reaches 0, the packet is dropped (and an ICMP packet may be sent to original sender).

## Slide 23: TTL reason
Q: What is the role of the TTL field?
A: To prevent packets from looping forever if there is a “routing loop” – forwarding tables on neighboring routers (mistakenly) send the packet back and forth to each other forever.

## Slide 24: &-ing process
Q: Could you go over a few examples of the &-ing process used in forwarding tables?
A: Sure… let’s look at section 22.6 and 22.7.

## Slide 25: Implications of lost packets
Q: What does an internet users actually experience when datagrams are lost? Is it errors, slow internet, or something else?
A: Depends on the application. If the application does not care about lost datagrams, then maybe nothing out of the ordinary is experienced. If the application requires all data be there, then you’ll get slower response times from the network, etc. This is determined by the Layer 4 protocol in use.