## Slide 1: Ch. 23, 25, 26 Q and A NAT, UDP, TCP
Victor Norman
IS333
Spring 2016

## Slide 2: NAT
What Comer calls NAPT, everyone else calls NAT.
Private (non-routable) addresses:
  Only used behind a NAT or on private networks.
  Can be subnetted.
  172.16/12 – 16 contiguous class B blocks?
    172.16, 172.17, 172.18, … 172.31.
NAT has a “private” (or “LAN”) side and a “public” (or ”WAN”) side.
Breaks the rule about the src and dest IP addresses in a packet never being changed as the packet is forwarded.

## Slide 3: What fields change for NAT?
Q: Can you show us on the board what fields NAPT changes as it forwards packets?
A: Sure!

## Slide 4: NAT Set up
Suppose we have a router doing NAT: half is the “public side”, IP address 77.78.79.80; other half is the “private side”, 192.168.0.1.
Host 192.168.0.111 sends packet to cnn.com @ 157.166.226.25, port 80.
  Host chooses source port 30000.
NAT makes entry in its table when first packet is sent.

## Slide 5: Why do you need to change the port in NAT?
Q: Why is the src IP address changed in NAT?
A: Because the src IP is a private, non-routable IP address, and used by many machines in private networks all over the known universe.
Q: Why do you need to change the port in NAT?
A: It is used as the key to distinguish return packets – to figure out which machine to forward to (because multiple machines behind the NAT can send to the same destination IP address).

## Slide 6: Why was NAT created?
Q: Why was NAT created?
A: So that one IP address can be given to a company/entity and yet, many machines can access the Internet. I.e., to preserve IP addresses.

## Slide 7: Private to private connection?
Q: Can a machine, with IP address m behind a NAT send messages to a machine with IP address d behind a NAT?
A: No (in general). What IP address would m use as the destination of the packets? If it used d, then that address is unroutable. If it used the WAN-side IP address of the d’s NAT, then how would the NAT know who to send the packet on to?

## Slide 8: UDP
Q: Is UDP layer 4?
A: Yes.
Q: Since UDP deals with applications, does that mean it is layer 5?
A: No. It is layer 4. It provides connection-less, unreliable delivery – same as IP. But, it is the layer that demultiplexes the received data to the multiple layer 5 protocols that use IP. This is done with the ports.

## Slide 9: Message-oriented interface
Q: What does it mean that UDP has a message-oriented interface?
A: It means when a program (at layer 5) tells UDP (at layer 4) to send data, the data is sent in one message to the destination. (We’ll see that TCP uses a different paradigm.)

## Slide 10: Fragmenting UDP?
Q: Multiple people asked about UDP fragmentation. Is it done or not?!
A: UDP does not do fragmentation. You can send a 64KB UDP message. It will be handed to IP below it, and IP will fragment it to fit into the MTU of the network it will be sent out on. The receiving IP layer will reassemble the 64KB packet before handing it back up to the receiving UDP layer.

## Slide 11: UDP
Q: What functionality does UDP provide that IP does not already provide?
A: Identification of the payload being carried at layer 5.
I.e., a port # so that it can hand the data off to an application.
I.e., demultiplexing.

## Slide 12: UDP used?
Q: Is UDP used today?
A: Yes, it is. It is used by
DNS (domain name resolution). It is used for
games
etc.
Q: Why is it used?
A: 1) Efficiency. It adds almost no functionality/overhead on top of IP. 2) You can broadcast a UDP message (because UDP is connectionless).

## Slide 13: Bad checksums
Q: What happens when a UDP packet is received with a bad checksum?
A: The packet is dropped. End of story.

## Slide 14: Pseudo-headers
Q: We all have lots of questions about pseudo-headers! Answer them!
A: No. They are not part of the learning objectives.

## Slide 15: What are the important characteristics of TCP?
Connection-oriented
Point-to-point
Full duplex
Reliable
Stream
Uses ports to identify applications using TCP.

## Slide 16: What does TCP assume it gets from the layer below?
Connection-less
Point-to-point
Simplex
Unreliable delivery
Message/packet based.

## Slide 17: What does connection-oriented mean?
End points must communicate first and set up the virtual connection.
No data is sent until that’s finished.
End points must gracefully tear down the connection.

## Slide 18: What does a Virtual Connection mean?
The endpoints set up and maintain all the state of the “connection” – the middle devices (routers, NATs, etc.) know nothing about it.
As opposed to a circuit through a network in which all devices must participate.

## Slide 19: What does point-to-point mean?
One application talks to one application
  one IP/port to one IP/port
Note: multiple TCP connections can go to the same IP/port. A connection is defined by the 4-ple.

## Slide 20: What does full duplex mean?
Both applications on the endpoints can transmit at the same time.
When a TCP connection is setup, it is full duplex – i.e., each endpoint can stream data.
  If you only want to stream one direction, you have to close the other half – although ACKs, etc., will still be sent.

## Slide 21: What does reliable delivery mean?
Gets the data there
  quickly
  correctly (without errors)
  in order
  completely

## Slide 22: What kinds of problems does TCP have to be able to handle?
Very unreliable delivery from IP.
  Duplicate packets.
  Packets out of order.
  Errors in packets.
Differing speeds of end points.
End point reboot.
Delay from when network changes radically.

## Slide 23: How does TCP handle all this?
Unreliable delivery from IP?:
  checksum the data (eliminate bad data)
  keep track of which bytes have been sent and which have been received, and resend missing bytes
  “positive acknowledgement and retransmission”
  A timer is started for each packet that is sent.
    if the timer expires for an ACK is received for the packet, the packet is resent.

## Slide 24: How does TCP handle all this? (part 2)
Different speeds of end points?:
  (Two problems: how much data an end point can handle at once, and how long it takes to handle it.)
  End points constantly communicate how much more data they can still handle at that time (called “window advertisement”).
  This is “flow control”.

## Slide 25: How does TCP handle all this? (part 3)
End point reboot? (Or application on an endpoint restarts.)
  Every connection is given a unique identifier and packets with that id are only accepted.

## Slide 26: How does TCP handle all this? (part 4)
Delay from network changes radically: consider this:
  end points want to get data through as fast as possible (in general).
  Usually end points want data to flow consistently, not bursty.
  When network “goes down” for a bit, the more data that is “in transit”, the more has to be retransmitted.
  This problem is very complex. Called “congestion control”.

## Slide 27: Congestion Detection
Congestion is detected by…
  increased round-trip time (data  ACK) (due to reduced throughput)
  timeouts (due to lost packets, perhaps)
The reaction is to reduce the window size and increase the per-packet timeout value.

## Slide 28: Congestion Collapse
Q: What is congestion collapse?
A: Congestion collapse is when congestion happens in a bottleneck in the network (usually a router), and the router discards packets. When the endpoints detect it, they retransmit, which only makes more traffic at the bottleneck, which causes more dropped packets and more retransmits. …

## Slide 29: Flow control vs. Congestion Control
Flow control via a sliding window allows multiple packets (“segments”) to be sent before any ACK is received. This increases bandwidth utilization (i.e., “speed”).
Congestion control reduces the amount of traffic being sent to avoid congestion collapse.
Both are done by manipulating the window size on a TCP connection.
Also, the ACK timer timeout value can be changed.
  ”Adaptive retransmission”.

## Slide 30: TCP fight between performance and reliability
(Section 26.6, 26.7)
We want our data to flow quickly AND reliably.
Increase window size  data rate increases.
Increase window size  chance of congestion increases.
Congestion  retransmitted packets  more congestion.
  “Congestion collapse.”

## Slide 31: TCP and IP
Q: What is the relationship between TCP and IP?
A: A TCP header and payload is the payload of an IP packet. The IP packet’s type field says it is carrying TCP. In other words, TCP is encapsulated in IP.
TCP builds a virtual connection between the endpoints, using the unreliable IP. IP is responsible for moving the packets to the destination machine.

## Slide 32: Fragmenting IP and TCP
Q: If a packet carrying TCP is fragmented during delivery, and one fragment is lost, how does TCP handle this?
A: 1) IP does fragmentation, when a packet is too large for one hop across the network.
2) If the fragment is lost, IP gives up on the packet and drops it.
3). If the TCP sender does not get an Ack before it times out, it resends the packet (which will get fragmented again).
4) When all fragments are received, the data is sent up to the TCP layer. It will then send an Ack.

## Slide 33: Stream protocol
Q: What does it mean that TCP is a stream protocol?
A: When an application (layer 5) sends a UDP packet, the packet going across the wire contains all the data from the application, in one chunk.
When it sends data using TCP, TCP is free to send as many or few bytes in a packet as it feels it can. The receiver also gets as many bytes at a time as TCP can give it.
The data “flows” from sender to receiver, but the endpoints don’t know how the data is “chunked” when sent across the network.

## Slide 34: Congestion control
Q: Could you explain how TCP controls congestion better? How does reducing the buffer size or window size reduce the data rate? Wouldn't it still send packets of the same size? Can the window size get bigger if there is little traffic or is it initialized to a maximum size?
A: The window size will be decreased  one packet can carry all the data for that window  fewer packets generated  less contribution to congestion. TCP also increases the timeout values.
TCP slowly increases the window size when it doesn’t encounter congestion.

## Slide 35: Flow Control
Q: Is flow control used quite often?
A: Yes: flow control is built into TCP. It, as well as, congestion control, are implemented with the sliding window feature.

## Slide 36: Calvin and Congestion Control
Q: Does Calvin use any of these dynamic congestion control methods?
A: Yes! You use it too – in the TCP/IP software in the OS on your machines.
And Calvin’s firewalls/etc. change some values to slow down youtube bandwidth, etc… 

## Slide 37: Lost window/segment
Q: If data lost in TCP, does the specific segment, or the whole window have to be retransmitted?
A: A window in TCP is a number of bytes, not packets (Comer used packets as an illustration). So, if a segment (a packet) is lost, that segment must be retransmitted.

## Slide 38: Handling reboots/outages
Q: What would happen if a connection was interrupted by an outside glitch on one of the computers (e.g., power outage)?
A: The TCP sender will stop receiving ACKs, will retransmit a few times, and then give up and return an error to the application.

## Slide 39: 3-way Handshake
Q: Can you explain the 3-way handshake more?
A: Yes! The initiator sends a SYN packet (a packet with the SYN flag set), and includes its ID and window size. The responder sends a SYN-ACK response including its ID and window size. The initiator sends an ACK back. (And, I think it piggybacks data in that packet.)

## Slide 40: Old Slides

## Slide 41: Multiple machines with same IP
Q: Does NAPT mean that many hosts could actually have the exact same IP address, say 10.0.0.1, but they are connected to different NATs, which have different IP addresses?
A: Yes. Most (all?) home routers do NAT, and your local home network is 192.168.0/24 or 192.168.1/24 or 10.0.0/8… So many many machines on the Internet have the same IP address but are hidden behind NATs.

## Slide 42: NAT in lab?
Q: In lab on Friday, were we dealing with NAT/NAPT and global & private addresses switching from 10.x.x.x and 153.106.117.x?
A: Nope. No NAT was being done. Just multiple networks connected to a multi-homed host, on which we configured IP forwarding.

## Slide 43: UDP Pseudo-header
Q: Can you explain pseudo headers a little more? How are they different than regular headers?
A: A pseudo-header is not actually sent over the network. It is built in the software when a UDP packet is sent/received. The software just reads the fields it needs from the IP header and uses those fields when calculating its checksum.

## Slide 44: UDP Checksum
Q: How does the UDP checksum work exactly?
A: It uses 16-bit, 1s-complement checksum: you take all 16-bit values and add them up. When you get an overflow, you add 1. Then, at the end you invert all bits.
Q: Does it make the header longer?
A: Yes: 16 bits longer. It is a field in the header.

## Slide 45: UDP Messages
Q: I was surprised that when UDP sends a block of data it is placed into a single message and not broken up and fragment like what we have learned in the past. Is this really the best idea? What about spacing and if a message is too large?
A: This is how it works. When your code does a write() on a UDP socket, the bytes you provide are sent, without delay.
A message can be up to 64K in size, and will be fragmented if needed (by IP).

## Slide 46: Unreliability
Q: In modern systems and networks, how often is it that a packet, like a UDP packet, doesn't reach its destination or is corrupted, or something like that? Is it common, uncommon, or what? And what sort of things contribute to this problem?
A: Packets definitely do get dropped. Routers get overloaded and packets get dropped. Also, radiation, etc., does corrupt packets.

## Slide 47: UDP end-to-end or connectionless?
Q: I thought parts of the stack were either 'end to end' or connectionless. The text seems to indicate that UDP is both. Please explain.
A: A protocol is either connectionless or connection-oriented. UDP is connectionless, and end-to-end. End-to-end means that the endpoints (hosts) communicate and the middle machines (routers) don’t do anything (routers operate at layer 3 and don’t route based on layer 4).

## Slide 48: UDP control messages?
Q: Do applications need to exchange UDP control messages before exchanging data?
A: No! That’s what makes UDP connectionless. An client that is going to send a UDP message to a server just sends it. The server does not know it is coming until it arrives. When a server receives a UDP message it gets the source address/port and the data. The next message could be from a different machine.

## Slide 49: UDP vs. TCP
Q: Are there any advantages to using UDP over TCP or another layer 4 protocol?
A: UDP is low overhead and efficient. But, unreliable.

## Slide 50: UDP port 80?
Q: The book gave examples that UDP uses port 7 and 37. Is port 80 one of those too or is that something completely different?
A: Port 80 would work. Anything from 0 to 65535. Theoretically, UDP port 80 identifies the layer 5 data as being http protocol. I’m not sure any one uses http over udp, though.